TAKS REVIEW

Mini-Objective 4(D):  Investigate and demonstrate mechanical advantage and efficiency of various machines, such as levers, motors, wheels and axles, pulleys, and ramps.

THE BARE MINIMUM

Machines

- machine: a device for making work easier

- this is done by  	(1) increasing the applied force or

        - (2) increasing the distance over which the force is applied or

        - (3) changing the direction of the force

- effort force: force put into a machine

- resistance force: the force the machine applies

Ideal Machines

input work = Win = Fe x de

output work = Wout = Fr x dr

Win = Wout

Mechanical Advantage

- mechanical advantage: the # of times a machine multiplies the effort force

- Ideal Mechanical Advantage (IMA): mechanical advantage for a machine with no friction

Efficiency

- efficiency: a measure of how much of the work put into a machine is changed into useful output; a ratio of Wout to Win

efficiency

- efficiency of a machine is always less than 100%.  (You lose work (energy) mainly due to friction.)

# Text boxes

OBJ 5: Motion, Forces, and Energy